## Slide 1: Boosting Lying Posture Classification with Transfer Learning
EMBC’2022

## Slide 2: Overview
Wristband
Chest belt
Thigh belt
Lying posture classification
  Chest belts, thigh integrated accelerometers raise some issues which wristbands do not.

## Slide 3: Why Lying Posture Is Important?
Lying postures provide-
  Important clinical information about subjects' mobility
  Risk factor for developing hospital acquired pressure injuries
  Information of sleep quality

## Slide 4: Drawbacks of other instruments
Camera based lying posture
  Imposes privacy concerns
Multi-sensor wearable systems
  Uncomfortable to wear
Pressure-mats
  Expensive to deploy at mass scale
Chest belts
  Causes sleep disturbance
Load sensors
  Non-invasive but expensive and requires calibration
issues

## Slide 5: Motivation for Wristband sensor
Wrist worn system guarantees
  No privacy issues
  No discomfort, easy to carry
  No sleep disturbance
  Not too expensive
However, directly using wrist worn sensor data raises accuracy issues due to presence of noise
*ET refers to ensemble tree, AdaLSTM refers to LSTM with adaptive learning rate
Low accuracy

## Slide 6: General Framework
or synthetic

## Slide 7: General Framework

## Slide 8: Mapping model
Called sequence to sequence mapping
2 different models were used
  LSTM seq2seq Regression
  LSTM seq2seq Encoder-Decoder
LSTM seq2seq regression
LSTM seq2seq Encoder-Decoder
Uses bidirectional LSTM to capture data from both direction
6 layers
Aims to minimize RMSE between input and output
Specs: max_epoch=100, Adam optimizer, batch_size=20, lr=0.01, decay rate=0.99
Also uses bidirectional LSTM
11 layers
Aims to minimize RMSE between input X and output X̂
Specs: max_epoch=100, Adam optimizer, batch_size=20, lr=0.01, decay rate=0.99

## Slide 9: Deep Classifier
AdaLSTM Network
  LSTM with adaptive learning rate
  Minimizes the classification error
Specifications
  Epoch=100, initial lr=0.01, decay rate=0.99,
  batch-size=27, Adam optimizer,
  softmax output activation
Bi-LSTM
(10 units)
Fully-connected
Fully-connected
Fully-connected
output
softmax

## Slide 10: Dataset
2 datasets were used
Class-Act dataset
  12 subjects, 9 acc sensors (chest, l-r thigh, l-r ankle, l-r arm, l-r wrist), sampled at 50 Hz
  Lying supine, lying prone, lying left side
Combined Class-Act dataset and Daily & Sports Activities dataset
  8 subjects, 5 IMU sensors (chest, l-r thigh, , l-r wrist), sampled at 25 Hz
For combining, Class-Act dataset was under sampled
Window size = 20 seconds

## Slide 11: Results

## Slide 12: Results